# Cisco IPv6 Configuration Commands:

6 March 2006

## Basic Commands:

To enable routing of IPv6 packets – required to enable IPv6 on a router:

Router(config)# ipv6 unicast-routing

To enable IPv6 on an interface:

Router(config-if)# ipv6 enable

To add an IPv6 address to an interface:

ipv6 address <address>/<prefix> [link-local] [eui-64]

To leave the interface unnumbered:

ipv6 unnumbered eth 0/0

## IPv6 Enabled Commands:

ping ipv6 <ipv6adr>

traceroute ipv6 <ipv6adr>

telnet <ipv6adr>

ssh [-l <userid>] [-c <des|3des>] [-o numberofpasswdprompts <#>] [-p <port#>] <ipv6addr> [command]

show ip ssh

ip http server

dns lookup

tftp

## Neighbor Discovery:

To adjust the Router Advertisement intervals:

ipv6 nc reachable-time <#>

ipv6 nd ra-interval <#>		default is 200 seconds

ipv6 nd ra-lifetime <#>		default is 1800 seconds (30 minutes)

ipv6 nd ns-interval <#>		default is 1000 milliseconds

ipv6 nd suppress-ra

ipv6 nd managed-config-flag

ipv6 nd other-config-flag

To adjust the lifetimes for the prefix:

ipv6 nd prefix-advertisement <routing-prefix>/<length> <valid-lifetime> <preferred-lifetime> [onlink] [auto-config]

ipv6 nd prefix-advertisement FEC0::C0A8:20C0/123 0 0 autoconfig

Valid lifetime = how long the node’s address remains in the valid state – after that it is invalid

Preferred lifetime = how long the stateless autoconfig address remains preferred – less than or equal to the valid lifetime - If preferred-lifetime = 0 then this router is not preferred

Off-link = sets the L-bit to OFF – default setting is to have the L-bit set to ON

No-autoconifg = sets the A-bit to OFF – default setting is to have the A-bit set to ON

No-advertise = the specified prefix cannot be used for stateless autoconfiguration – the prefix is not included in RA messages – default is to have this flag turned OFF

To remove an advertised prefix:

no ipv6 nd prefix <ipv6-prefix>

To turn off Router Advertisements:

no suppress-ra

Duplicate Address Detection (DAD):

ipv6 nd dad attempts <#>		disabled with a setting of “0”

Router Redirection:

ipv6 redirects

ipv6 icmp error-interval msec

## Other Commands:

ip domain lookup

ip name-server <ipv6addr>

ipv6 host <NAME> [<port>] <ipv6addr1> <ipv6addr2> . . .

ipv6 neighbor <ipv6addr> Ethernet 0 <macaddr>

## Basic Show Commands:

show ipv6 ?

show ipv6 interface <interface-name-number> [prefix]

show interface

show ipv6 neighbors [ <ipv6addr-or-name> | <interfacetype-number> ]

show ipv6 mtu

show ipv6 protocols

show ipv6 interface [brief]

show ipv6 traffic

show ipv6 route

show ipv6 routers

show bgp

show bgp summary

show bgp ipv6 unicast neighbor <addr> routes

show bgp ipv6 unicast neighbor <addr> advertised

## Basic Debug Commands:

debug ipv6 ?

debug ipv6 packet

debug ipv6 icmp

debug ipv6 nd

ping ipv6 <ipv6addr>

traceroute ipv6 <ipv6addr>

clear ipv6 ?

clear ipv6 neighbors

## Cisco Express Forwarding:

ipv6 cef

ipv6 cef distributed

show ipv6 cef . . .

show cef

debug ipv6 cef [drops | events | hash | receive | table]

## Routing Commands:

ipv6 route <ipv6prefix>/<prefix-length> [ <next-hop-IPv6-addr> | <interface-type-#> ] [AD#]

show ipv6 route [connected | local | static | rip | bgp | isis | ospf]

show ipv6 route <ipv6prefix>/<prefix-length>

## RIPng:

To enable RIPng:

Router(config)# ipv6 router rip <TAG>

To enable RIPng on an interface:

Router(config-if)# ipv6 rip <TAG> enable

To originate the default router (::/0) out an interface:

Router(config-if)# ipv6 rip <TAG> default-information originate

Router(config-rtr)# distance <#>

Router(config-rtr)# distribute-list prefix-list <prefixlistNAME> [in | out] <interface>

Router(config-rtr)# metric-offset <#>

Router(config-rtr)# poison-reverse

Router(config-rtr)# split-horizon

Router(config-rtr)# port <UDP-port> multicast-group <mcastaddr>

Router(config-rtr)# timers <update> <expire> <holddown> <garbage-collect>

Router(config-rtr)# redistribute [ connected | isis | ospf | static | bgp | rip <TAG> ] [metric <metric>] [level-1 | level-1-2 | level-2] [route-map <NAME>]

## RIPng Show Commands:

show ipv6 route

show ipv6 rip [database] [next-hops]

show ipv6 protocols

## RIPng Debug Commands:

debug ipv6 rip <interface>

debug ipv6 routing

clear ipv6 rip <TAG>

## OSPF Commands:

Router(config)# ipv6 router ospf <process-ID>

Router(config-rtr)# router-ID <ipv4addr>

Router(config-rtr)# area <v4areaID> range <ipv6addr/length>

Router(config)# interface ethernet 0

Router(config-if)# ipv6 ospf <process-ID> area <v4areaID>

Router(config-rtr)# redistribute [bgp | isis | rip | static]

## OSPF Show Commands:

show ipv6 ospf <processID>

show ipv6 ospf database

show ipv6 ospf <processID> database link

show ipv6 ospf <processID> database prefix

show ipv6 ospf route ospf

## OSPF Debug Commands:

clear ipv6 ospf <processID>

## OSPF Example:

interface Ethernet 0

ipv6 address 2001:100:1::1/64

ipv6 enable

ipv6 ospf 100 area 0

interface Ethernet 1

ipv6 address 2001:200:2::1/64

ipv6 enable

ipv6 ospf 100 area 1

ipv6 router ospf 100

router-id 10.1.1.1

area 1 range 2001:200:FFFF:1::1/64

## EIGRP Commands:

interface FastEthernet 0/0

ipv6 enable

ipv6 eigrp 10

ipv6 bandwidth-percent eigrp <as-number> <percent>

ipv6 summary-address eigrp <as-number> <ipv6-address> [admin-distance]

ipv6 authentication mode eigrp <as-number> md5

ipv6 authentication key-chain eigrp <as-number> <key-chain>

!

ipv6 router eigrp 10

router-id 10.1.1.1

stub [receive-only | connected | static | summary | redistributed]

log-neighbor-changes

log-neighbor-warnings [seconds]

metric weights tos k1 k2 k3 k4 k5

!

show ipv6 eigrp interfaces

show ipv6 eigrp neighbors detail

show ipv6 eigrp topology

show ipv6 eigrp traffic

clear ipv6 eigrp [as-number] [neighbor [ipv6-address | interface-type interface-number]]

debug eigrp fsm

debug eigrp neighbor [siatimer] [static]

debug eigrp packet

debug eigrp transmit [ack] [build] [detail] [link] [packetize] [peerdown] [sia] [startup] [strange]

debug ipv6 eigrp [as-number] [neighbor ipv6-address | notification | summary]

## BGP4+ Commands:

Enable BGP-4 on the router:

router bgp <ASN>

Turns off BGP IPv4 peering

no bgp default ipv4 unicast

Establish a BGP4+ neighbor:

neighbor <ipv6addr> remote-as <ASN>

neighbor <ipv6addr> update-source <interface>

neighbor <ipv6addr> soft-reconfiguration inbound

neighbor <ipv6addr> password 5 <password>

Address Families:

address-family ipv6 unicast …

neighbor <ipv6addr> activate

exit-address-family

To enable a prefix-list for a BGP-peer:

neighbor <ipv6addr> prefix-list <NAME> [in | out]

ipv6 prefix-list <NAME> [ seq [#] ] [ permit | deny ] <IPv6prefix/length> [ ge <min-value> ] [ le <max-value> ]

Route Maps:

neighbor <ipv6addr> route-map <NAME> [in|out]

route-map <NAME> [ permit | deny ] <seq#>

match ipv6 [<ipv6addr> | next-hop | route-source] prefix-list <prefixlistNAME>

set ipv6 next-hop <ipv6addr> <link-local-addr>

set local-pref 120

Redistribution:

redistribute [bgp | connected | isis | ospf | rip | static] [metric <metric>] [route-map <routemapNAME>]

## BGP4+ Show Commands:

show ipv6 route bgp

show ipv6 neighbors

show bgp neighbors

show bgp ipv6 [summary]

show bgp ipv6 [<ipv6prefix/length> | community | community-list | dampened-paths | regexp <regexp> | summary ]

show ipv6 prefix-list [summary | detail] <prefixlistNAME>

## BGP4+ Debug Commands:

debug bgp ipv6

clear bgp ipv6 [ * | ASN | <ipv6addr> | dampening | external | flap-statistics | <peer-group-name> ]

## BGP4+ Example:

interface Ethernet0

ipv6 address 5f00:0100:0:0:1::1 80

!

router bgp 100

no bgp default ipv4-unicast

neighbor 5f00:0100:0:0:2::1 remote-as 101

aggregate-address 2001:420:2000::/42 summary-only

!

address-family ipv6

neighbor 5f00:0100:0:0:2::1 activate

neighbor 5f00:0100:0:0:2::1 prefix-list bgp-in in

neighbor 5f00:0100:0:0:2::1 prefix-list aggregate out

network 5f00:0100:0:0:1::/40

exit-address-family

ipv6 prefix-list aggregate seq 5 deny 3FFE:C00::/24 ge 25

ipv6 prefix-list aggregate seq 10 permit ::/0 le 48

!

ipv6 prefix-list bgp-in seq 5 deny 5F00::/8 le 128

ipv6 prefix-list bgp-in seq 10 deny ::/0

ipv6 prefix-list bgp-in seq 15 deny ::/1

ipv6 prefix-list bgp-in seq 20 deny ::/2

ipv6 prefix-list bgp-in seq 25 deny ::/3 ge 4

ipv6 prefix-list bgp-in seq 30 permit ::/0 le 128

## IPv6 Access Control Lists:

ipv6 access-list <NAME> [permit|deny] <src-prefix[*]> | any | host <hostip> … <dest-prefix[*]> | any | host <hostip> … [log | log-input]

ipv6 access-list BLAH deny fec0:0:0:2::/64 * any

ipv6 access-list BLAH permit any

Apply ACL to an interface:

Router(config-if)# ipv6 traffic-filter <ACL-NAME> [in | out]

For 6Bone – minimum prefix to announce:

3ffe::/16

3ffe:0800::/28

2000::/3		- 6to4

For 6Bone – prohibits advertisements of these:

fe80::/10		- link local

fec0::/10		- site local

::1/128		- loopback

::0/128		- default route

ff00::/8		- multicast

::/96		- ipv4 compatible addresses

::ffff/96		- ipv4 mapped addresses

View the ACLs:

show ipv6 access-list <ACL-MANE>

clear ipv6 access-list <ACL-NAME>

debug ipv6 packet [access-list <ACL-NAME>] [detail]

## Configured Tunnel Router Commands:

Router 1:

interface tunnel 0

ipv6 address 3ffe:b00:c18:1::3/27

tunnel source 192.168.1.1

tunnel destination 192.168.2.1

tunnel mode ipv6ip [auto-tunnel]

Auto-tunnel if used for automatic tunnels

Router 2:

interface tunnel 0

ipv6 address 3ffe:b00:c18:1::2/27

tunnel source 192.168.2.1

tunnel destination 192.168.1.1

tunnel mode ipv6ip [auto-tunnel]

## 6to4 Tunnel Router Commands:

Router 1:

interface Ethernet 0

ip address 192.168.1.1 255.255.255.0

ipv6 address 2002:c0a8:0101:1::/64 eui-64

interface tunnel 0

no ip address

ipv6 unnumbered Ethernet 0

tunnel source Ethernet 0

tunnel destination 192.168.2.1

tunnel mode ipv6ip 6to4

Router 2:

interface Ethernet 0

ip address 192.168.2.1 255.255.255.0

ipv6 address 2002:c0a8:0201:1::/64 eui-64

interface tunnel 0

no ip address

ipv6 unnumbered Ethernet 0

tunnel source Ethernet 0

tunnel destination 192.168.2.1

tunnel mode ipv6ip 6to4

For a 6to4 Relay add the following route:

ipv6 route ::/0 <ipv6addr of 6to4 relay>

## 2 Router Example:

hostname Alpha

ipv6 unicast-routing

interface Ethernet0

description connected to A-LAN

no ip address

no ip directed-broadcast

ipv6 enable

ipv6 address FEC0::C0A8:20C1/123

ipv6 nd ra-interval 20

ipv6 nd ra-lifetime 180

ipv6 rip brest-lab enable

interface Serial1

description connected to Chi Ser1

bandwidth 4000000

no ip address

no ip directed-broadcast

encapsulation ppp

ipv6 enable

ipv6 address FEC0::C0A8:2025/126

ipv6 nd ra-interval 20

ipv6 nd ra-lifetime 180

ipv6 nd prefix-advertisement FEC0::C0A8:20C0/123 0 0 autoconfig

no suppress-ra

ipv6 rip brest-lab enable

clockrate 4000000

hostname Chi

ipv6 unicast-routing

interface Ethernet0

description connected to Core-LAN

no ip address

no ip directed-broadcast

ipv6 enable

ipv6 address FEC0::C0A8:10C2/123

ipv6 nd ra-interval 20

ipv6 nd ra-lifetime 180

ipv6 rip brest-lab enable

interface Serial1

description connected to Alpha Ser1

bandwidth 4000000

no ip address

no ip directed-broadcast

encapsulation ppp

ipv6 enable

ipv6 address FEC0::C0A8:2026/126

ipv6 nd ra-interval 20

ipv6 nd ra-lifetime 180

ipv6 nd prefix-advertisement FEC0::C0A8:10C0/123 0 0 autoconfig

no suppress-ra

ipv6 rip brest-lab enable